## Slide 1: Flow chamber

## Slide 2: Flow chamber

## Slide 3: Flow chamber

## Slide 4: Flow chamber

## Slide 5: Flow chamber

## Slide 6: Flow chamber

## Slide 7: Flow chamber

## Slide 8: Array configuration

## Slide 9: Flow chamber
to pump
Specs
Sample volume: 20µl
Pump (suction):
  Peristaltic (manual start/stop)
  Syringe (manual and program)
Channel:
  Width: 1mm
  Height: 100µm
Step 1
Probe + buffer (high FRET)
Wash both channels with buffer
Step 2
Probe + comp. strand (low FRET)
Wash with buffer
Caveat
Anti-sticking: tween added to buffer
Diffusion repeatability:
  Repeat Step 1 multiple times to study variations
Time scale
  1-30s with 1s resolution

## Slide 10: Flow chamber building protocol
Courson DS, Rock RS (2009) Fast Benchtop Fabrication of Laminar Flow Chambers for Advanced Microscopy Techniques. PLoS ONE 4(8)

## Slide 11: Preliminary experiments
First crude flow chamber built
Tested with peristaltic pump
Results
Sample does not flow evenly in the two channels
Flow is not uniform (in time)

## Slide 12: Stop flow approach
Pump
INPUT: Syringe-pump
The flow is forced to be the same on both channels
OUTPUT:
Stopping syringe fixes the volume
Mixer
T-junction
“arrow” junction
Problems
High volume 500µL

## Slide 13: Minimize the sample volume
Samples
Buffer
Buffer
Syringe buffer
Syringe sample
Push
Fixed
Syringe buffer
Syringe sample
Fixed
Push
Flow
chamber

## Slide 14: What we want to investigate?
Dynamics of short dsDNA hybridization in freely diffusing conditions
Since the sample is freely diffusing we necessary have a mixing phase
The mix phase can be fully characterized (time-constant, variability)
We measure a process transient: high FRET to low FRET
If no difference in transient:
the process is diffusion limited (if D=const. the speed does not change)
If big difference in transient:
the process is driven by hybridization dynamics
Otherwise:
the process is regulated by both diffusion and hybridization dynamics